## Slide 2: MIMDAS
The Philosophy, Development and Deployment
A Story of a Queensland Based Geophysical Success
Nick Sheard RPGeo, AIG, ASEG, CTM
Sort of Geophysicist, Ex Exploration Manager, Consulting Geoscientist
Geophysics for Geologists
Seminar Program – 30 Nov. 2018

## Slide 3
MIMDAS
An acronym for :
Mount Isa Mines Distributed Acquisition System
MIMEX the Exploration Arm of MIM Holdings
Taken over by XSTRATA in 2003

## Slide 4: The Story : Hopefully not too geophysical
Why
The early days
The Bars and Beers
How did a bunch with bugger all expertise build it ?
How did we minimise costs ?
Deployment ?
Conclusion

## Slide 5
Electrical Geophysics was not providing optimal answers
MIMEX was not happy with
  the resolution
  the penetration
  the data quality
  the presentation
  the interpretation
Basically we wanted to Reduce the Drilling Risk
What we said in 1993 :
And getting abused by Geologists
Why ?

## Slide 6
We needed to know why geophysics was so bad and could we improve it ?
A couple us including Gary Fallon, Phil Andrews, Grant Kensington and myself went bush and just measured input waveforms of commonly available equipment
Results were appalling wave forms were nothing like what the manufacturer claimed
The Early Days – before conception

## Slide 7
?- CRAPPY DATA
CAN WE DO BETTER -?
BLOODY OATH !!
A Bush Scene near Cloncurry
July 1993

## Slide 8
How could you expect to get good interpretation if the input signal is not what you are told it is
Why ?
Supposedly a square wave
input
But actually a sort of square wave with noise and overshoots

## Slide 9
An inhouse TEM system
Went to manufacturers asking for a quantum better hardware
Result :
Manufacturers just offered an update of current system
So could MIMEX do it internally ?
MIMTEM was sort of conceived

## Slide 10
Met John Kingman in a bar in Arizona
He wanted to build a super IP System
MIMEX was going to build an EM system
After a few beers we realised we were talking about a super voltage amplifier
If designed properly and given good software could do all sorts of electrical geophysics
The Bars and Beers
This is where drinking and bars come into it

## Slide 11
Concept
Better drilling success with better gear – be in front of the pack
Keep costs low by involving many Companies / AMIRA/ CSIRO / Universities
Inhouse gathering of all software into one toolbox
Keep John Kingman as consultant in Brisbane
Could start immediately
Got ok go for it !!
A few more bars/beers
Went To Management – Ross Fardon
Dec 1994

## Slide 12
A proprietary ground geophysical data acquisition system
Distinctive Characteristics :
  A General Purpose Multichannel Array style System e.g. 100 channels
  Full Time Series
  24 bit A/D
  Very High S/N
  Advanced Signal Processing
  Interpretation Friendly
The Concept
MIMDAS Specs were conceived - 1995

## Slide 13
Why Multichannel ?
An Array
Electrical noise – eg tellurics, thunderstorms 1000;s km away, culture (mains) etc will all be measured at one point in time and therefore removed easier
RECORDING UNIT
SENSORS

## Slide 14: Field data - MT 2 Individual channels showing simultaneity of noise
Spheric
48 kHz sampling

## Slide 15
Closer channel spacing
Better resolution
    for e.g.- magnetics
200m line spacing
Why Multichannel?
20m line spacing
RESULT
better targeting reduced drilling risk

## Slide 16
Why Data Quality ?
A CHARGEABILITY CURVE
10 PTS
4096 PTS

## Slide 17
Bit = 65,536
24 Bit = 16,777,216
Or 256 times the resolution
Resolution
Why 24bit ?

## Slide 18
80 mV - Raw Full-Duty Cycle
0.4 mV - Vp
2 mV - Stacked & Processed
Half-Duty Response Estimate
14 V - IP decay
Ie 14 x 1 millionth of a volt
Why Uniform Sampling ?
EG 50 hz rejection

## Slide 19
INPUT WAVE
Sample wave
Deconvolve
Change to new wave
Deconvolve ground response with same process
New INPUT WAVE
Why Uniform Sampling and
Measuring Input Wave ?

## Slide 20
How did a bunch with bugger all expertise build it ?
March 1995 Kingman and I met Reftek a nitche Seismic Hardware Developer
Paul Passmore the owner of Reftek reckoned he could build :
  A low-cost single channel a/d amplifier
  Expandable to at least 100 channels
  24 bit A/D
  Full Time Series
  Very High S/N
Cost $200,000 BUT MIM owns the rights for hard rock exploration but he can use hardware for other uses

## Slide 21
The First Box

## Slide 22
Meanwhile focusing on
Interpretation & Visualization
Pseudosections -
who can interpret them ?
2 d Models
very useful
Resistive
Conductive
1000m
0m
DEPTH
m
3d physical property maps

## Slide 23
The MIMEX Model
Look globally for interpretation software
  IP, EM, MT in particular
Do deals for collaborative R and D to keep costs down
Undertake inhouse interpretive software
  Eg strap on Inversion software to existing software
Combine all into a MIMEX toolbox
Not really much an addition to existing budget
Est $100k / Yr

## Slide 24
Back to Hardware
Field Trials
First field trials in Dallas are Dec 1995
  Results – needed lots more work
Second field trials in Mt Isa June 1996
  Results – great at first
  All went to Irish club to cellebrate
  John K slept in Caravan
Next day – it did not work !!
Back to drawing board and Texas

## Slide 25
The Mk1 System
The Prototype
MIMDAS FIELD TRIALS - JUNE 1997

## Slide 26
MARK 2 MIMDAS IN OPERATION NW QLD
Sept 1998
52 Channels now
operating and it worked !!

## Slide 28
THE BLACK BOX THAT WORKS

## Slide 29
GEORGE FISHER 3D DISPLAY
3D Conductivity plot
from Magnetotelluric
data.
GEORGE FISHER
SURVEY

## Slide 30: Ernest Henry IP Data : MIMDAS v. WMC 300 m South of Current Pit
TECHNICAL -GEOPHYSICS Slide 4.3
CHARGEABILITY
OBSERVED RESISTIVITY
OBSERVED CHARGEABILITY
CONVENTIONAL - ZONGE SURVEY
0 m
700 m
Top of EH
300 m

## Slide 31: Ernest Henry MT
BLUE -resistive
PROCESSING AND INTERPRETATION
3D CONDUCTIVITY PLOT
RED - conductive
DEPTH
0M
1000M

## Slide 32
Electrical Property Mapping Using MIMDAS
Mt Isa Region :
AIM :
assist in finding more ISA ore bodies
integrated approach
geology / geochemistry surface mapping
magnetics / gravity
3d electrical mapping – very difficult conditions
  mod’ conductive overburden (20 ohm m)
  conductive host (15 ohm m)
  graphitic shales all over the place (sub 1 ohm m)
an iterative interpretation procedure

## Slide 33
500 m
150 m
Standard IP in conductive region
Equiv. to 100m
dip - dip
Real IP
MIMDAS
500 m Penetration
COMPARISON - INVERTED IP Data

## Slide 34
It Finally Worked So Off around the World

## Slide 38
MIMDAS Costs - very much guestimates
Intitial Hardware - $200,000
Interp’R and D - $400,000 i.e. 4 yrs at $100k / yr
Sensors - $100,000
Labour field trials etc - $ 1,000,000
100 Channels @$2000 - $200,000
Total est - A$2million
R and D Tax incentive value (125%) = $2.5 m
Company Tax Rate 36% in 1998
So Tax relief = $0.9m
So final cost est $1m

## Slide 39
Conclusion
Progression at MIMEX :
in 1994 standard electrical geophysical practice was ORDINARY
  drill risk high - due to poor interp’
  interp’ poor due to poor data / difficult software
  thus restricted to”easy” regions
needed better tools – acquisition / visualisation / interpretation
contractors were not cashed up – advances were upgrades
MIMEX designed and built new distributed acquisition system
modified, built and bought interp’ and visualisation s/w
result MIMDAS
  deep looking / high resolution complete system

## Slide 40
  Designed at MIM Brisbane
  Built by Reftek in Dallas
  Deployed Globally by MIM
  Now owned and operated by GRS a Qld Geophysical Service Group
  Can do IP, EM Magnetotellurics, Seismics and any other type of electrical geophysics
  Many thanks to the MIMEX Geophysical team who supported this effort
I need to note that I do not have any financial interest in GRS or MIMDAS
MIMDAS Conclusion :

## Slide 41
MIMEX’S
R&D TEAM

## Slide 42
Good Technology will help us
DRILL SMARTER
Apply the correct technology
or overload your exploration budget with waste